## Slide 1: Network
Introduction to
Computer Networks
Slide Source: Cisco Networking

## Slide 2: Networking Today
Network has no boundary and supports the way we:
  Learn
  Communicate
  Work
  Play

## Slide 3: LANs and WANs
Local Area Networks
  Spans across small geographical area
  Interconnects end devices
  Administrated by a single organization
  Provide high speed bandwidth to internal devices
WAN Area Networks
  Interconnects LAN
  Administrated by multiple service providers
  Provide slower speed links between LANS
Can you name more network types?

## Slide 4: Network Components

## Slide 5: Network Components
End Devices
  Either the source or destination of a message
Intermediary Network Devices
  Connect multiple individual networks to form an internetwork
  Connect the individual end devices to the network
Network Media
  Provide the pathway for data transmission
  Interconnect devices

## Slide 6: Copper Media
Shielded Twisted Pair (STP) Cable
Unshielded Twisted Pair (UTP) Cable
Coaxial Cable

## Slide 7: UTP Cable

## Slide 8: UTP Connectors

## Slide 9: Creation of Internet, Development of TCP/IP
The first packet switching network and predecessor to today’s Internet was the Advanced Research Projects Agency Network (ARPANET), which came to life in 1969 by connecting mainframe computers at four locations.
ARPANET was funded by the U.S. Department of Defense for use by universities and research laboratories. Bolt, Beranek and Newman (BBN) was the contractor that did much of the initial development of the ARPANET, including creating the first router known as an Interface Message Processor (IMP).
In 1973, Robert Kahn and Vinton Cerf began work on TCP to develop the next generation of the ARPANET. TCP was designed to replace ARPANET’s current Network Control Program (NCP).
In 1978, TCP was divided into two protocols: TCP and IP. Later, other protocols were added to the TCP/IP suite of protocols including Telnet, FTP, DNS, and many others.

## Slide 10: The OSI Reference Model

## Slide 11: The TCP/IP Reference Model
Notes: 3.2.4.3 The TCP/IP Protocol Model

## Slide 12: Comparing the OSI and TCP/IP Models

## Slide 13: Benefits of Using a Layered Model

## Slide 14: Establishing the Rules
An identified sender and receiver
Common language and grammar
Speed and timing of delivery
Confirmation or acknowledgment requirements

## Slide 15: Network Protocols
How the message is formatted or structured
The process by which networking devices share information about pathways with other networks
How and when error and system messages are passed between devices
The setup and termination of data transfer sessions

## Slide 16: TCP/IP Protocol Suite and Communication

## Slide 17: Message Formatting and Encapsulation
Example: Personal letter contains the following elements:
Identifier of the recipient’s location
Identifier of the sender’s location
Salutation or greeting
Recipient identifier
The message content
Source identifier
End of message indicator

## Slide 18: Protocol Data Units (PDUs)
Data
Segment
Packet
Frame
Bits

## Slide 19: Protocol Encapsulation

## Slide 20: Protocol De-encapsulation

## Slide 21: MAC and IP Addresses
PC1
192.168.1.110
AA-AA-AA-AA-AA-AA
PC2
192.168.1.111
BB-BB-BB-BB-BB-BB
FTP Server
192.168.1.9
CC-CC-CC-CC-CC-CC
R1
192.168.1.1
11-11-11-11-11-11
ARP
Request
S1
R1

## Slide 22: Default Gateway

## Slide 23: Communicating with Device / Same Network

## Slide 24: Communicating Device / Remote Network

## Slide 25: Address Resolution Protocol (ARP)

## Slide 26: ARP Operation
ARP Table
Maps data link layer address to destination IPv4 address.
As a node receives frames from the media, it records the source IP and MAC address as a mapping in the ARP table.
ARP Request
Layer 2 broadcast to all devices on the Ethernet LAN.
The node that matches the IP address in the broadcast will reply.
If no device responds to the ARP request, the packet is dropped because a frame cannot be created.

## Slide 27: LAN and WAN Frames
Notes: 4.4.4.5 LAN and WAN Frames

## Slide 28: Ethernet Frame format
Preamble and Start Frame Delimiter Fields –
Used for synchronization between the sending and receiving devices.
Length/Type Field –
Defines the exact length of the frame's data field; describes which protocol is implemented.
Data and Pad Fields –
Contains the encapsulated data from a higher layer, an IPv4 packet.

## Slide 29: The Network Layer
The network layer, or OSI Layer 3, provides services to allow end devices to exchange data across the network. To accomplish this end-to-end transport, the network layer uses four basic processes:
Addressing end devices
Encapsulation
Routing
De-encapsulating
Notes: 6.1.1.1 The Network Layer

## Slide 30: Network Layer Protocols
IP version 4 (IPv4)
IP version 6 (IPv6)
Notes: 6.1.1.2 Network Layer Protocols

## Slide 31: Best Effort Delivery

## Slide 32: IP – Media Independent

## Slide 33: Encapsulating IP

## Slide 34: IPv4 Packet Header

## Slide 35: Unicast Address

## Slide 36: Broadcast Address

## Slide 37: Multicast Address
Multicast MAC address is a special value that begins with 01-00-5E in hexadecimal
Range of IPV4 multicast addresses is 224.0.0.0 to 239.255.255.255

## Slide 38: Sample IPv4 Headers in Wireshark

## Slide 39: Limitations of IPv4
IP Address depletion
Internet routing table expansion
Lack of end-to-end connectivity
Notes: 6.1.4.1 Limitations of IPv4

## Slide 40: IPv6
Increased address space
Improved packet handling
Eliminates the need for NAT
Integrated security
4 billion IPv4 addresses 4,000,000,000
340 undecillion IPv6 addresses 340,000,000,000,000,000,000,000,000,000,000,000,000

## Slide 41: IPv4 and IPv6 Headers

## Slide 42: IPv6 Packet Header
Version | Traffic Class |  | Flow Label |  |  | 
Payload Length |  |  |  | Next Header | Hop Limit | 
Source IP Address |  |  |  |  |  | 
Destination IP Address |  |  |  |  |  | 
Byte 1
Byte 2
Byte 3
Byte 4