## Slide 1: IPv6 Network Addresses
IPv4 Issues The IPv6
Source: Cisco networking

## Slide 2: The Need for IPv6
IPv6 is designed to be the successor to IPv4.
Depletion of IPv4 address space has been the motivating factor for moving to IPv6.
Projections show that all five RIRs will run out of IPv4 addresses between 2015 and 2020.
With an increasing Internet population, a limited IPv4 address space, issues with NAT and an Internet of things, the time has come to begin the transition to IPv6!
IPv4 has a theoretical maximum of 4.3 billion addresses, plus private addresses in combination with NAT.
IPv6 larger 128-bit address space provides for 340 undecillion addresses.
IPv6 fixes the limitations of IPv4 and includes additional enhancements, such as ICMPv6.

## Slide 3: IPv4 and IPv6 Coexistence
The migration techniques can be divided into three categories:
Dual-stack, Tunnelling, and Translation.
Dual-stack: Allows IPv4 and IPv6 to coexist on the same network. Devices run both IPv4 and IPv6 protocol stacks simultaneously.
Dual-stack

## Slide 4: IPv4 and IPv6 Coexistence (cont.)
Tunnelling: A method of transporting an IPv6 packet over an IPv4 network. The IPv6 packet is encapsulated inside an IPv4 packet.
Tunnelling

## Slide 5: IPv4 and IPv6 Coexistence (cont.)
Translation: The Network Address Translation 64 (NAT64) allows IPv6-enabled devices to communicate with IPv4-enabled devices using a translation technique similar to NAT for IPv4. An IPv6 packet is translated to an IPv4 packet, and vice versa.
Translation
Notes: 8.2.1.2 IPv4 and IPV6 Coexistence (cont.)

## Slide 6: IPv6 Address Representation
128 bits in length and written as a string of hexadecimal values
In IPv6, 4 bits represents a single hexadecimal digit, 32 hexadecimal value = IPv6 address
  2001:0DB8:0000:1111:0000:0000:0000:0200
  FE80:0000:0000:0000:0123:4567:89AB:CDEF
Hextet used to refer to a segment of 16 bits or four hexadecimals
Can be written in either lowercase or uppercase

## Slide 7: IPv6 Addressing Rule 1- Omitting Leading 0s
The first rule to help reduce the notation of IPv6 addresses is any leading 0s (zeros) in any 16-bit section or hextet can be omitted.
01AB can be represented as 1AB.
09F0 can be represented as 9F0.
0A00 can be represented as A00.
00AB can be represented as AB.
Notes: 8.2.2.3 Rule 1 – Omitting Leading 0s

## Slide 8: IPv6 Addressing Rule 2 - Omitting All 0 Segments
A double colon (::) can replace any single, contiguous string of one or more 16-bit segments (hextets) consisting of all 0’s.
Double colon (::) can only be used once within an address otherwise the address will be ambiguous.
Known as the compressed format.
Incorrect address - 2001:0DB8::ABCD::1234.
Notes: 8.2.2.4 Rule 2 – Omitting All 0 Segments

## Slide 9: IPv6 Addressing Rule 2 - Omitting All 0 Segments (cont.)
Example #1
Example #2

## Slide 10: Types of IPv6 Addresses IPv6 Prefix Length
IPv6 does not use the dotted-decimal subnet mask notation
Prefix length indicates the network portion of an IPv6 address using the following format:
  IPv6 address/prefix length
  Prefix length can range from 0 to 128
  Typical prefix length is /64

## Slide 11: Types of IPv6 Addresses IPv6 Address Types
There are three types of IPv6 addresses:
Unicast
Multicast
Anycast.
Note: IPv6 does not have broadcast addresses.

## Slide 12: Types of IPv6 Addresses IPv6 Unicast Addresses
Unicast
  Uniquely identifies an interface on an IPv6-enabled device.
  A packet sent to a unicast address is received by the interface that is assigned that address.

## Slide 13: IPv6 Unicast Addresses (cont.)

## Slide 14: IPv6 Unicast Addresses (cont.)
Global Unicast
  Similar to a public IPv4 address
  Globally unique
  Internet routable addresses
  Can be configured statically or assigned dynamically
Link-local
  Used to communicate with other devices on the same local link
  Confined to a single link; not routable beyond the link
Notes: 8.2.3.3 IPv6 Unicast Addresses (cont.)

## Slide 15: IPv6 Unicast Addresses (cont.)
Loopback
  Used by a host to send a packet to itself and cannot be assigned to a physical interface.
  Ping an IPv6 loopback address to test the configuration of TCP/IP on the local host.
  All-0s except for the last bit, represented as ::1/128 or just ::1.
Unspecified Address
  All-0’s address represented as ::/128 or just ::
  Cannot be assigned to an interface and is only used as a source address.
  An unspecified address is used as a source address when the device does not yet have a permanent IPv6 address or when the source of the packet is irrelevant to the destination.
Notes: 8.2.3.3 IPv6 Unicast Addresses (cont.)

## Slide 16: IPv6 Unicast Addresses
Unique Local
  Similar to private addresses for IPv4.
  Used for local addressing within a site or between a limited number of sites.
  In the range of FC00::/7 to FDFF::/7.
IPv4 Embedded
  Used to help transition from IPv4 to IPv6.
Notes: 8.2.3.3 IPv6 Unicast Addresses (cont.)

## Slide 17: IPv6 Link-Local Unicast Addresses
Every IPv6-enabled network interface is REQUIRED to have a link-local address
Enables a device to communicate with other IPv6-enabled devices on the same link and only on that link (subnet)
FE80::/10 range, first 10 bits are 1111 1110 10xx xxxx
1111 1110 1000 0000 (FE80) - 1111 1110 1011 1111 (FEBF)
Notes: 8.2.3.4 IPv6 Link-Local Unicast Addresses

## Slide 18: IPv6 Link-Local Unicast Addresses (cont.)
Packets with a source or destination link-local address cannot be routed beyond the link from where the packet originated.
Notes: 8.2.3.4 IPv6 Link-Local Unicast Addresses

## Slide 19: IPv6 Unicast Addresses Structure of an IPv6 Global Unicast Address
IPv6 global unicast addresses are globally unique and routable on the IPv6 Internet
Equivalent to public IPv4 addresses
ICANN allocates IPv6 address blocks to the five RIRs
Notes: 8.2.4.1 Structure of an IPv6 Global Unicast Address

## Slide 20: Structure of an IPv6 Global Unicast Address (cont.)
Currently, only global unicast addresses with the first three bits of 001 or 2000::/3 are being assigned

## Slide 21: Structure of an IPv6 Global Unicast Address (cont.)
A global unicast address has three parts: Global Routing Prefix, Subnet ID, and Interface ID.
Global Routing Prefix is the prefix or network portion of the address assigned by the provider, such as an ISP, to a customer or site, currently, RIR’s assign a /48 global routing prefix to customers.
2001:0DB8:ACAD::/48 has a prefix that indicates that the first 48 bits (2001:0DB8:ACAD) is the prefix or network portion.

## Slide 22: Structure of an IPv6 Global Unicast Address (cont.)
Subnet ID is used by an organization to identify subnets within its site
Interface ID
  Equivalent to the host portion of an IPv4 address.
  Used because a single host may have multiple interfaces, each having one or more IPv6 addresses.

## Slide 23: Static Configuration of a Global Unicast Address
Notes: 8.2.4.2 Static Configuration of a Global Unicast Address

## Slide 24: IPv6 Unicast Addresses Static Configuration of an IPv6 Global Unicast Address (cont.)
Windows IPv6 Setup
Notes: 8.2.4.2 Static Configuration of an IPv6 Global Unicast Address (cont.)

## Slide 25: IPv6 Unicast Addresses Dynamic Configuration of a Global Unicast Address using SLAAC
Stateless Address Autoconfiguraton (SLAAC)
A method that allows a device to obtain its prefix, prefix length and default gateway from an IPv6 router
No DHCPv6 server needed
Rely on ICMPv6 Router Advertisement (RA) messages
IPv6 routers
Forwards IPv6 packets between networks
Can be configured with static routes or a dynamic IPv6 routing protocol
Sends ICMPv6 RA messages
Notes: 8.2.4.3 Dynamic Configuration of a Global Unicast Address using SLAAC

## Slide 26: IPv6 Unicast Addresses Dynamic Configuration of a Global Unicast Address using SLAAC (cont.)
The IPv6 unicast-routing command enables IPv6 routing.
RA message can contain one of the following three options:
  SLAAC Only – Uses the information contained in the RA message.
  SLAAC and DHCPv6 – Uses the information contained in the RA message and get other information from the DHCPv6 server, stateless DHCPv6 (for example, DNS).
  DHCPv6 only – The device should not use the information in the RA, stateful DHCPv6.
Routers send ICMPv6 RA messages using the link-local address as the source IPv6 address
Notes: 8.2.4.3 Dynamic Configuration of a Global Unicast Address using SLAAC (cont.)

## Slide 27: Dynamic Configuration of a Global Unicast Address using SLAAC (cont.)
Notes: 8.2.4.3 Dynamic Configuration of a Global Unicast Address using SLAAC (cont.)

## Slide 28: Dynamic Configuration of a Global Unicast Address using DHCPv6 (cont.)
Dynamic Host Configuration Protocol for IPv6 (DHCPv6)
Similar to IPv4
Automatically receives addressing information, including a global unicast address, prefix length, default gateway address and the addresses of DNS servers using the services of a DHCPv6 server.
Device may receive all or some of its IPv6 addressing information from a DHCPv6 server depending upon whether option 2 (SLAAC and DHCPv6) or option 3 (DHCPv6 only) is specified in the ICMPv6 RA message.
Host may choose to ignore whatever is in the router’s RA message and obtain its IPv6 address and other information directly from a DHCPv6 server.
Notes: 8.2.4.4 Dynamic Configuration of a Global Unicast Address using DHCPv6 (cont.)

## Slide 29: Dynamic Configuration of a Global Unicast Address using DHCPv6 (cont.)
Notes: 8.2.4.4 Dynamic Configuration of a Global Unicast Address using DHCPv6 (cont.)

## Slide 30: EUI-64 Process
EUI-64 Process
Uses a client’s 48-bit Ethernet MAC address and inserts another 16 bits in the middle of the 46-bit MAC address to create a 64-bit Interface ID.
Advantage is that the Ethernet MAC address can be used to determine the interface; is easily tracked.
EUI-64 Interface ID is represented in binary and comprises three parts:
24-bit OUI from the client MAC address, but the 7th bit (the Universally/Locally bit) is reversed (0 becomes a 1).
Inserted as a 16-bit value FFFE.
24-bit device identifier from the client MAC address.
Notes: 8.2.4.5 EUI-64 Process or Randomly Generated

## Slide 31: EUI-64 Process
Notes: 8.2.4.5 EUI-64 Process or Randomly Generated

## Slide 32: EUI-64 Process
Notes: 8.2.4.5 EUI-64 Process or Randomly Generated (cont.)

## Slide 33: Static Link-local Addresses
Configuring Link-local
Notes: 8.2.4.7 Static Link-local Addresses

## Slide 34: Static Link-local Addresses (cont.)
Configuring Link-local
Notes: 8.2.4.7 Static Link-local Addresses (cont.)

## Slide 35: Verifying IPv6 Address Configuration
Each interface has two IPv6 addresses -
global unicast address that was configured
one that begins with FE80 is automatically added as a link-local unicast address
Notes: 8.2.4.8 Verifying IPv6 Address Configuration

## Slide 36: Verifying IPv6 Address Configuration (cont.)
Notes: 8.2.4.8 Verifying IPv6 Address Configuration (cont.)

## Slide 37: Assigned IPv6 Multicast Addresses
IPv6 multicast addresses have the prefix FF00::/8
There are two types of IPv6 multicast addresses:
  Assigned multicast
  Solicited node multicast
Notes: 8.2.5.1 Assigned IPv6 Multicast Addresses

## Slide 38: Assigned IPv6 Multicast Addresses (cont.)
Two common IPv6 assigned multicast groups include:
  FF02::1 All-nodes multicast group –
    All IPv6-enabled devices join
    Same effect as an IPv4 broadcast address
  FF02::2 All-routers multicast group
    All IPv6 routers join
    A router becomes a member of this group when it is enabled as an IPv6 router with the ipv6 unicast-routing global configuration mode command.
    A packet sent to this group is received and processed by all IPv6 routers on the link or network.
Notes: 8.2.5.1 Assigned IPv6 Multicast Addresses (cont.)

## Slide 39: Assigned IPv6 Multicast Addresses (cont.)
Notes: 8.2.5.1 Assigned IPv6 Multicast Addresses (cont.)